# Multiscreen (Actions)

The information is relevant for version 2.9.34 and later.

Description of Multiscreen Actions.
## Acknowledge Alarm
Alert confirmation by the operator.
Parameters
No parameters.
## Silence Alarm
Silence all alerts.
Parameters
No parameters.
## Enable Alarm
Set alerts for the selected window.
Parameters
- Param1 - window name mask (wildcard).
- Param2 - comma-separated alert type. Possible values:
  - still - Still Frame
  - black - Black Frame
  - higher - audio overload
  - lower - audio silence
  - xmlrpcdisconnect - connection lost
## Disable Alarm
Disable alerts for the specified window.
Parameters
- Param1 - window name mask (wildcard).
- Param2 - alert type, comma-separated. Possible values:
  - still - Still Frame
  - black - Black Frame
  - higher - audio overload
  - lower - audio silence
  - xmlrpcdisconnect - connection lost
## Set Active Window
Switches the sound from the selected window to the multiscreen output (the window is framed).
Parameters
- Param1 - window name.
- Param2 - audio output template name (Audio Layout Name).
## Next Window
Make the next window active.
Parameters
No parameters.
## Previous Window
Make the previous window active.
Parameters
No parameters.
## Next Audio Layout
Selects the next audio output template for the active window (Set Active Window).
Parameters
No parameters.
## Previous Audio Layout
Selects the previous audio output template for the active window (Set Active Window).
Parameters
No parameters.
## Next Caption Stream
Selects the next available caption stream for the active window (Set Active Window).
Parameters
No parameters.
## Previous Caption Stream
Selects the previous available caption stream for the active window (Set Active Window).
Parameters
No parameters.
## Set Caption Stream
Sets the caption stream for the specified window.
Parameters
- Param1 - window name.
- Param2 - caption stream type:
  - CEA-708,
  - CEA-608,
  - CEA-608L21,
  - Teletext
- Param3 - stream or page number:
  - 1-16 for 708,
  - 1-4 for 608,
  - 100-8ff for Teletext
## Set Caption Detect
Controls detecting captions in the active window (Set Active Window).
Parameters
- Param1
  - 0 - disable.
  - 1 - enable.
## Set Captions Enabled
Controls caption preview in the active window (Set Active Window).
Parameters
- Param1
  - 0 - disable.
  - 1 - enable.
## Display Caption Stream Info
Displays brief information on currently displayed captions.
Parameters
No parameters.
## Alarm Sound On
Turns on the sound alert. The audio file is specified in the module settings: Administrator Control Panel→Manage→Multiscreens→Multiscreen_N→Playout Parameters→General→Alarm sound.
Parameters
No parameters.
## Alarm Sound Off
Turns off the sound alert.
Parameters
No parameters.