# Anchors
Starting from version 2.3.12, Graphics Editor has the function of anchoring coordinates of a graphic object vertically and horizontally with other objects in the graphic composition.
The media_db_1080i50_20180307_2392 demo database contains an example of how the Anchors function works.

ObjectAnchorDemo elements are anchored, which allows them to adapt to text content specified through parameterization from the playlist.
## Setting
To anchor object A to object B, open Anchors in object A properties. After anchoring, resizing object B, or moving it will affect object A.

Option	Value
Vert	Vertical anchoring – selecting the parameter of the initial object to be anchored: / Disable – anchoring inactive / Top edge – anchor the top edge of object A, / Bottom edge – anchor the bottom edge of object A, / Height – anchor the height of object A.
bind to (Vert)	Vertical anchoring – selecting the parameter of the object to anchor to: / Top edge – to the top edge of object B, / Bottom edge – to the bottom edge of object B, / Height – to the height of object B.
Hor	Horizontal anchoring – selecting the parameter of the initial object to be anchored: / Disable – anchoring inactive / Left edge – anchor the left edge of object A, / Right edge – anchor the right edge of object A, / Width – anchor the width of object A.
bind to (Hor)	Horizontal anchoring – selecting the parameter of the object to anchor to: / Left edge – to the left edge of object B, / Right edge – to the right edge of object B, / Width – to the width of object B.
of	Setting the name for the target object to anchor to (object B)
offset	Setting the anchoring offset, in pixels. A positive value sets the indent, a negative value sets the overlap.