# Live Stream Input Function (live capture of the real-time Internet streams)

Description is valid for software version 2.11.0 and newer.

In 2.11.0 version, the ability to capture network streams directly in software modules was added.
Most software components that accept video streams as input are not capable of directly capturing real-time network streams.
Modules that support this input mode are:
- Playout;
- Recorder;
- Background layer of the Program module;
- Profanity Delay;
- Time Shift;
- Multiviewer individual Windows;
- Stream Object in the media database, which can be directly placed in a playlist.
This feature eliminates the need for a Capture module to capture a network stream in the corresponding module. For modules that support Compressed Workflow, this feature also allows you to input pre-compressed live streams and work without decoding or re-encoding the video. It also allows direct monitoring of network streams in Multiviewer.
Supported streaming formats include:
- MPEG2TS via UDP or SRT
- HLS
- RTMP
- Youtube
- Various streaming platforms
## Input URL Format
The input URL format is compatible with input URL of ffmpeg stream.
### UDP
UDP URL syntax: udp://hostname:port[?options]
Examples:
- udp://225.1.100.1:1234 - receiving multicast stream.
- udp://225.1.110.1:2000?localaddr=192.168.0.20 - receiving multicast stream over the selected local interface. It can be useful when more than one interface is used in the system.
- udp://225.1.110.1:4900?sources=10.1.0.1 - receiving multicast stream sent from the specified addresses.
### SRT
SRT URL syntax: srt://hostname:port?mode=caller&passphrase=string&latency=microseconds, where:
- mode - specifies the type of connection used. Specify one of the following options in the mode parameter: caller, listener or rendezvous.
- passphrase - specifies the password to receive the stream.
- latency - specifies the maximum buffer size available for SRT packet management.
Examples:
- srt://11.22.33.44:8000?mode=caller - receiving the SRT stream with the connection type specified.
- srt://11.22.33.44:8000?mode=caller&passphrase=string - receiving the SRT stream with the connection type and password specified.
### RTMP
RTMP URL Syntax: %rtmp://[username:password@]server[:port][/app][/instance][/playpath]
Examples:
- rtmp://11.22.33.44:1935/appname/streamname - receiving the RTMP stream.
- rtmp://username:password@11.22.33.44:1935/appname/streamname - receiving the RTMP stream with login and password specified.