# GPI Board (Actions)

The information is relevant for version 2.9.34 and later.

Description of GPI Board Actions.
## Set pin
Sets the output status for the selected pin.
Parameters
- Param1 - pin number (starts with 1).
- Param2 - new pin status:
  - 0, off or false - disable
  - 1, on or true - enable
  - other values - no changes
## Pulse pin
Sends a pulse of the specified duration to the pin output.
Parameters
Param1-
## Trigger Handler
Launches the action handlers (pins) when an input signal is detected.
Parameters
- Param1 pin number (starts with 1).
- Param2 - new pin status:
  - 0, off or false - disable
  - 1, on or true - enable
  - other values - no changes
## Do Command
Perform a command that is typical for a particular type of hardware.
Parameters
- Param1 - command name:
  - sGPI for Louth decoder
  - set for Ember+
### For Louth decoder (Param1=sGPI)
- Param2 - Key
- Param3 - ID
- Param4 - Segment
- Param5 - Title
- Param6 - on_air
### For Ember+ (Param1=set)
- Param2 - Pin number
- Param3 - Value
- Param4 - not used
- Param5 - not used
- Param6 - not used