# Playout (REST API)
Module description	REST API

Queries to control the Playout module.
## Retrieving Current Loudness Parameters
The command allows retrieving the current Loudness status.

http://localhost:7901/playout?module_id=<N>&command=get_loudness
Parameter description:
POST – HTTP POST query.
<IP_ADDR> – server IP address.
<N> - Playout service sequence number (starts with 1).
get_loudness - command to retrieve current Loudness parameters.
Example of a generated response:
enabled: ON preset: 0 gain: 0.9 before: -22.0 LUFS after: -22.6 LUFS

Description of parameters in the server response:
Parameter	Description

enabled	Status of the EBU-R128 Loudness normalizer at the time of the query: ON - enabled, OFF - disabled.

preset	Number of the currently used preset. Possible values: 0-3 (0 = Preset1 and so on). Preset values are specified in Playout module settings on the EBU-R128 Loudness tab. Presets are selected manually on the Status tab of the control panel, or using the EBU-R128 Loudness Preset Action.

gain	Amplification value at the time of the query: / value <1 - signal attenuation occurs, / value >1 - signal amplification occurs.

before	Current level value at the normalizer input in LUFS.

after	Current level value at the normalizer output, in LUFS.	The field displays the average value of 3 Integration Periods specified in Playout module settings on the EBU-R128 Loudness tab.